## Slide 1: Perf-Board Tips
Andrew Tubesing
University of St Thomas

## Slide 2: Perf-board Tips
Resist the urge
to wire on the bottom

## Slide 3: Perf-board Tips
Wiring on bottom is ok for special purposes, such as buses

## Slide 4: Per-board Tips
Route wires on top
whenever possible
Use multiple colors
All the same color is difficult to trace and troubleshoot

## Slide 5: Per-board Tips
Bend short wire tip over toward neighboring lead
Snip it where it touches neighboring lead
Solder the two pads and leads together
Treat wires like components:
Strip the end
Insert through neighboring hole

## Slide 6: Perf-board Tips
Know when to get a PCB!